## Slide 1
INVESTOR BRIEFING · ATREIDES 2 NM
Atreides.
Ready for 2 nm.
Where the SF16 accelerator stands, the $1.7M round that takes it to first 2 nm silicon, and the program beyond it.
superfloat.si
October 2026
SIGNAL FLOW / SF16
PE[3,7] · C ← C + A · B

## Slide 2: Superfloat spends every bit on value
02 / 14
01 / THE FORMAT
BF16 · 1/8/7
S
E
E
E
E
E
E
E
E
M
M
M
M
M
M
M
SF16 · 1 + 15
S
V
V
V
V
V
V
V
V
V
V
V
V
V
V
V
S sign · E exponent · M mantissa · V value, signed fixed point Q1.15
99.999%
of parameters in trained networks already sit inside [−1, 1]. The exponent pays for range they never use.
No exponent
hardware in the multiply-add: no align, no normalise, one pipeline stage on the partial-sum path.
SF4 to SF16
one format family at any width, converted exactly from standard floats. SF8 lands within 1% of SF16.

## Slide 3: Three chips signed off on SkyWater 130 nm
03 / 14
02 / PROVEN AT 130 NM
GPT-2 small, same RTL | SF16 | FP16 | BF16
Tile area | 1.40 mm² | 1.86 mm² | 1.63 mm²
Chip power, decode, 50 MHz | 251 mW | 460 mW | 441 mW
Energy per output token | 5.55 J | 10.17 J | 9.74 J
Energy per YOLOv8n image | 53 J | 98 J | 94 J
SAME CYCLES, LESS ENERGY
−45%
energy per token against FP16, and 43% against BF16, in prefill, decode and YOLOv8n alike.
Each chip: four tiles of 8×8 systolic arrays (256 MACs), a custom 16-bit ISA, SIMT threads. Zero violations in every sign-off check, timing met across nine corners. Next: ChipFoundry shuttle CI2612, tape-out 7 December 2026.
ChipFoundry OpenFrame v1, signed off 1 Oct 2026. Post-layout power and energy; only the PE, FMA and activation units differ.

## Slide 4: 2.5× the compute per watt of FP16
04 / 14
03 / MEASURED AT 2 NM
Chart: Compute per watt (16-bit TFLOPS/W)
| SF16 | FP16 | BF16
TFLOPS/W | 8.6 | 3.4 | 4.11
Chart: Compute per mm² (16-bit TFLOPS/mm²)
| SF16 | FP16 | BF16
TFLOPS/mm² | 60.1 | 35.4 | 40.7
TOP CLOCK
3.39 GHz
with the multiplier over two stages, against 3.01 GHz for FP16 and 3.03 GHz for BF16. SF16 has no float align or add stage to hold it back.
233 fJ per MAC against 589 (FP16)
v3 processing elements on the GT2N 2 nm predictive PDK (not a TSMC PDK): OpenROAD to global route, 0.7 V, typical corner, real GPT-2 operands at 2 GHz. Bit-exact at gate level.

## Slide 5: The lead holds at 45, 3 and 2 nm
05 / 14
04 / EVERY NODE
Chart: SF16 compute per watt, times FP16 and BF16
| 45 nm | 3 nm | 2 nm
vs FP16 | 2.88 | 2.65 | 2.53
vs BF16 | 2.44 | 2.24 | 2.09
HAMMERBLADE MANYCORE
All 180 GPT-2 prefill matrix multiplies bit-exact on a RISC-V manycore, 11% sooner to the first token.
ACCURACY
GPT-2 perplexity within 0.55% of FP32. Detection within about 4% of FP32; classification and video level or better.
Same flow and GPT-2 stimulus at every node. NanGate45 and GT3 are research PDKs, one corner each, global-route parasitics.

## Slide 6: A 10 mm² N2 shuttle chip comes first
06 / 14
05 / THE TEST CHIP
SF16
1.09 mm²
FP16
1.85 mm²
BF16
1.61 mm²
SRAM, 12 MB
2.5 mm²
Control core, clocking, test I/O
about 3 mm² (estimate)
Proves the SF16 matrix unit, SRAM and clock in TSMC silicon before the production mask set.
Compares all three formats on one die, one wafer: one 128×128 matrix unit each.
Yields dozens of dies from one shuttle; we plan around 40 for bring-up and validation.
Tapes out on the first 2027 N2 shuttle (March, if TSMC keeps its March and September runs).
Costs about $800K to $1.6M in silicon (estimate), about $21K to $40K a die.
Matrix-unit areas from the measured 2 nm blocks; SRAM at TSMC N2's published 38.1 Mb/mm². Floorplan drawn to scale.

## Slide 7: 800 mm², 1.73× the matrix compute of FP16
07 / 14
06 / THE PRODUCTION DIE
On-die SRAM, 3.22 GB
676 mm²
Matrix units
70 mm²
I/O and HBM PHYs 40 mm² · vector units, control, DMA, network 14 mm²
4,194
peak 16-bit TFLOPS from 64 matrix units, against 2,425 (FP16) and 2,818 (BF16) in the same 70 mm²
4.8 TB/s
from four HBM3E stacks, 144 GB, for what the 3.22 GB of SRAM cannot hold
1.66×
GPT-2 small decode at batch 1: 44,403 tokens/s against 26,743 for FP16
Before production tape-out: much wider vector units, faster weight loading for decode, and more capacity for long-context batches. Each applies to all three formats.
Modeled: 2 GHz, 700 W cap, roofline over matrix, vector, memory and power. Only the matrix units come from measured 2 nm blocks.

## Slide 8: Test chip in 2027, production from 2028
08 / 14
07 / THE PLAN
NOV TO DEC 2026
Start
Design-service partner, TSMC NDA, N2 PDK; reserve the shuttle slot; send the 2028 wafer forecast.
7 DEC 2026
130 nm tape-out
Three OpenFrame chips on ChipFoundry CI2612; parts back May 2027.
MARCH 2027
N2 test chip
Tape-out on the first 2027 N2 shuttle.
MID-2027
Bring-up
Dies back, measured against the 2 nm models. Second shuttle in September if a respin is needed.
Q4 2027
Production tape-out
The 800 mm² die on its own mask set.
2028
Year 1
1,000 N2 wafers, about 40,000 chips, first parts mid-year.
Why start now: N2 capacity is booked into 2028 and reserved about a year ahead with prepayment, so 2028's wafers must be requested before the test chip is back.

## Slide 9: Raising $1.7M to reach first 2 nm silicon
09 / 14
08 / THE ROUND
$1.7M
takes Atreides from signed-off 130 nm chips to measured 2 nm silicon on TSMC's N2 shuttle.
The production program follows first silicon (slide 10).
$1.2M
N2 shuttle silicon
About 10 mm², around 40 dies, March 2027 shuttle
$300K
Design-service NRE
PDK access, N2 sign-off and tape-out handling
$150K
Packaging and bring-up
Packaging, boards and lab bring-up for the test chips
$45K
130 nm shuttle
Three OpenFrame chips on ChipFoundry CI2612
Each line sits inside the readiness budget's ranges. Milestones: 130 nm tape-out Dec 2026, N2 test chip tape-out Mar 2027, dies back mid-2027.

## Slide 10: $29M to $70M to production tape-out
10 / 14
09 / THE FULL PROGRAM
Phase | What it covers | Estimate
130 nm shuttle | Three ChipFoundry OpenFrame chips at the published $14,950 | $45K
N2 test chip | 10 mm² shuttle silicon, packaging and boards, design-service allowance, respin reserve | $1.2M to $4.4M
Production tape-out | N2 mask set, IP licences, design-service, test program and probe cards | $23M to $59M
EDA tools | About 10 seats at $80K to $150K an engineer-year | $800K to $1.5M
Team | Six hires: three in VLSI, three in AI | $3.8M to $4.6M
Total |  | $29M to $70M
WHERE IT GOES
~70%
is the N2 mask set ($15M to $30M) and IP licences ($5M to $20M).
Design-service NRE has no public figure; it is an allowance until a partner quotes it.
The $1.7M round funds the 130 nm shuttle and the test chip at its base case. N2 figures are estimates; TSMC publishes no prices.

## Slide 11: About $3,550 per chip in year 1
11 / 14
10 / UNIT COST
Chart: Planning cost per 800 mm² chip (USD)
| Silicon | HBM3E ×4 | Packaging | Assembly, test
Plan, USD per chip | 750 | 1400 | 900 | 500
Per chip | Range
Silicon | $500 to $1,000
HBM3E, four 36 GB stacks | $920 to $1,840
CoWoS-class packaging | $600 to $1,200
Assembly and test | $370 to $600
Per chip, at the 40-die plan | $2,640 to $4,390
Year 1, 40,000 chips: $142M at plan ($106M to $176M), of which $30M is 1,000 N2 wafers.
Per chip at 40 good dies a wafer. HBM3E and CoWoS from public estimates; contract prices are confidential and rising.

## Slide 12: 1,000 wafers in 2028, 10× by 2032
12 / 14
11 / VOLUMES
Chart: N2 wafer starts per year (plan)
| 2028 | 2029 | 2030 | 2031 | 2032
N2 wafers | 1000 | 2000 | 3400 | 5800 | 10000
Year | Chips | Wafers
2028 | 40,000 | $30M
2029 | 80,000 | $60M
2030 | 136,000 | $102M
2031 | 232,000 | $174M
2032 | 400,000 | $300M
Plan targets, not orders. A 100 mm² edge die would give about 550 chips a wafer.
Chips at 40 good 800 mm² dies a wafer (30 to 60 across the yield range). Wafers at today's $30,000; TSMC raised 2026 prices 5 to 10%.

## Slide 13: Partners for access, sign-off, IP, packaging and test
13 / 14
12 / WHAT WE NEED
Foundry access
TSMC NDA and N2 PDK, the 2027 shuttle slot, and 2028 wafer allocation.
N2 sign-off
N2-certified EDA, DFM and timing, power and reliability sign-off.
Third-party IP
HBM3E PHY and controller, high-speed I/O, PLLs and clocking.
Packaging
Flip-chip for the test chip; a CoWoS-class interposer with four HBM3E stacks for production.
Test
Wafer sort, final test and probe cards, for dozens of dies and then 40,000 a year.
Quotes
Shuttle slot, mask set and 2028 wafers, to replace our public-report estimates.
We own architecture, RTL, verification and physical design. At first-year volume, a Taiwan design-service partner close to TSMC is the practical route; direct engagement as volumes grow.

## Slide 14
Intelligence.
At the bit level.
Alosh Denny · alosh@superfloat.si · superfloat.si
github.com/aloshdenny · superfloat, .llvm, .cuda, .gpu
October 2026